Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model: 	     		Indoor/Outdoor

- 82% Efficiency

- ASME Code Glass-Lined Cast Iron Headers

- ASME Code Copper-Fin Tube

- 125 lb. Pressure Relief Valve

- Small Footprint

- Unitherm Governor Anti-Condensation Control

- Internal Bypass for High Flow Rates (up to 125 gpm)

- Indoor/Outdoor

- Low NOx; ≤ 55ppm

#### Heat Exchanger

ASME Inspected and Stamped
160 PSIG

National Board Approved

Glass-lined Cast Iron Headers

Finned Tubing

Copper – Standard

Cupro Nickel – Optional

ASME Steel Tube Sheet

Silicone O-Rings

125 PSIG Pressure Relief Valve

Water Connections

Right Hand – Standard

Left Hand – Field Change

Flow Configuration – Two-pass

#### Controls

115/230V, 60Hz, 1 Ph Power Supply

115/230/24V Transformer

100% Pilot Shut-off

Electronic, Intermittent Ignition Pilot (IID)

High Limit Control

On/Off Switch

Flame Rollout Switch

Water Pressure Switch

Dual Electronic Temp Sensor

Digital Display With Diagnostics

#### Gas Control Train

Natural Gas

Combination Control Valve

On/Off Firing

ANSI Z21.56 Design Certified

#### Construction

Front Controls

Stainless Steel Burners

Polytuf Powder Coat Finish

Indoor/Outdoor

Vent Selection

Outdoor Stackless Top – Standard

Indoor Draft Diverter, Loose – Optional

D-2 Power Vent, Loose – Optional

Can be installed on combustible surfaces

ASME Digital Low NOx

Gas Pool Heaters	Model

# Text boxes

# ASME Digital

# Low NOx

# Gas Pool Heaters

# Models CR-207A – CR-407A

Shown with outdoor top

Proudly Assembled in the USA

Raypak, Inc. ( 2151 Eastman Avenue, Oxnard, CA  93030 ( (805) 278-5300 ( Fax (800) 872-9725 (  www.raypak.com

Raypak Canada Ltd. ( 2805 Slough St., Mississauga, Ontario, Canada L4T 1G2 ( (905) 677-7999 ( Fax (905) 677-8036 ( www.raypakcanada.com

| Heater Model | BTUH Input (000) | Dimensions (in.) | Shipping Weights (lbs) |
| --- | --- | --- | --- |
|  |  | Cabinet Width (A) | Flue Dia. (B) | Indoor Drafthood (C) | (J) | Gas Conn. | Water Conn. | With Stackless Top | With Indoor Drafthood |
| CR-207A | 199.5 | 20 | 6 | 55-5/8 | 11-3/4 | 3/4 | 2 | 193 | 12 |
| CR-267A | 266.0 | 23 | 7 | 56 | 11 | 3/4 | 2 | 216 | 15 |
| CR-337A | 332.5 | 26 | 8 | 57 | 10-5/8 | 3/4 | 2 | 238 | 17 |
| CR-407A | 399.0 | 29 | 9 | 58-1/2 | 12-1/8 | 3/4 | 2 | 256 | 20 |

Notes:

1.	Ratings are for natural gas and elevations up to 5,000 feet above sea level. For elevations over 5,000 feet, consult the factory.

2.	Manufactured under Patent  No. 3,623,458.