Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model:

Applications

- Radiant Heating

- Hydronic Space Heating

- Snow Melting

High Efficiency

Heating efficiencies meet or exceed NAECA standards.

Factory Installed Circulator and Bypass

Thermostatically-controlled circulator maintains proper flow through the boiler. As a packaged system, installation is fast and easy.

Electronic Ignition

Intermittent pilot ignition improves system efficiency by using fuel only when there is a call for heat.

Compact, Lightweight Design

Even the largest model slips easily into tight spaces.

Easy to Plumb, Easy to Service

Inlet and outlet water piping, gas connection, wiring and controls are all up front for easy access.

Safe Operation

Built-in manual reset safety sensors shut down the boiler in the event of a flame roll-out or flue gas spillage. Normal working pressure is 125 PSI max.

Fast Response Temperature Sensor

Electronic solid state auto-reset control shuts down the boiler in the event of over-heating caused by a low-flow condition.

#### Heat Exchanger

ASME Inspected and Stamped
160 PSIG

National Board Approved

Glass-lined Cast Iron Headers

Copper Finned Tubing

ASME Steel Tube Sheet

Silicone O-Rings

30 PSIG ASME Pressure Relief Valve

Temperature and Pressure Gauge

Cast Iron Pump – 120 VAC, Mounted

Bypass Assembly

#### Stainless Options

All Stainless Pump, 120 VAC, Mounted Stainless Fittings

#### Controls

120V, 60Hz, 1 Ø Power Supply

120/24V Transformer

Electronic, Intermittent Ignition
(IID) - Standard

- 100% Pilot Shut-off/Lockout (IID only)

High Limit Control

Operating Limit Control

Flow Sensor

Flue Gas Spillage Sensor

Flame Rollout Sensor

Automatic Vent Damper

Electronic Outdoor Reset Control

#### Gas Control Train

Fuel

Natural Gas

Propane Gas

Firing Mode

- On/Off - Models 42-66

- Two-stage Firing - Models 90-180

Combination Gas Valve

- Manual Shut-off

- Redundant Valve Features

- Gas Pressure Regulator

#### Construction

Indoor Construction

Enclosed Front Controls

Stainless Steel Burners

Polytuf Powder Coat Finish

Built-in Draft Diverter

Certified for combustible flooring

Raypak Residentials

Hydronic Heating Boilers	Model

Notes:

1.	Standard models, use “H-” prefix (e.g., H-0042); Non-ferrous models, use “HB-” prefix (e.g., HB-0042)

2.	Per Section 11.1.2 of the National Fuel Gas Code, derate the appliance firing rate 4% per 1,000 feet above sea level for installations above 2,000 feet.

# Text boxes

# Raytherm™ Residentials

## Hydronic Heating Boilers

## Models 42-180

Fig. #8942

AFUE Ratings

| Model | AFUE |
| --- | --- |
| 0042 | 84.0 |
| 0066 | 83.0 |
| 0090 | 82.7 |
| 0135 | 82.8 |
| 0180 | 83.2 |

Models 42, 66 & 90

Models 135 & 180

Raypak, Inc. ( 2151 Eastman Avenue, Oxnard, CA  93030 ( (805) 278-5300 ( Fax (800) 872-9725 ( www.raypak.com