Job:

Engineer:

Contractor:

Prepared By: 	     		Date:

Model:

Applications

- Radiant Heating

- Hydronic Space Heating

- Snow Melting

- DHW via indirect

High Efficiency

Infinitely modulating, Condensing design meets or exceeds Energy Star Standards.

Low Emissions

Low NOx design meets all current Green Legislation in North America.

Factory Installed Circulator

w/ Bypass and Condensate Siphon

Thermostatically-controlled circulator maintains proper flow through the boiler. As a packaged system, installation is fast and easy. Twin chamber ball type

Siphon, the best flue seal.

Electronic Ignition

Direct Spark Ignition

Compact, Lightweight Design

Mounts easily onto walls without heavy bracing.

Easy to Plumb, Easy to Service

Vent on top. Inlet and outlet water piping, gas connections, wiring and condensate drain at bottom. Controls are up front for easy access.

Safe Operation

Sealed combustion chamber runs cool and sensors shut down the boiler in the event of a fault.

Electronic Thermostat with Diagnostics

Electronic solid state thermostatic control operates the boiler in the most efficient manner. Faults are displayed on two digit display.

Whisper Quiet Operation

Less than 60 dba

DHW Temp Controller Up Front

#### Heat Exchanger

ASME Inspected and Stamped
45 PSIG

National Board Approved

Extruded 6063-T1 Aluminum Alloy Single Pass Heat Exchanger

45 PSIG ASME Pressure Relief Valve

Pressure Gauge

3 Speed Non-Ferrous Pump

120 VAC, Mounted

- Two Automatic Air Vents

#### Controls

120V, 60Hz, 1(Power Supply

120/24V Transformer

Electronic, Direct  Spark Ignition (DSI)

100% Flame Monitor Shut-off/Lockout

High Limit Control

Operating Limit Control

Pressure Switch

Condensate High Level Sensor

Flue Sensor

Flue Limit

#### Venting Options

AL29-4C Stainless Steel Vent

CPVC Plastic Vent

Polypropylene Plastic Vent

Concentric Vent or Twin Penetrations

Horizontal or Vertical Vent

Gas Control Train

Natural Gas (Propane Conversion

Kit w/ Every Unit)

4 to 1 Modulation

Zero Governor Gas Valve

Manual Gas Shut-Off Valve

Redundant Valve Feature

Negative Pressure Gas Regulator

#### Construction

Indoor Construction

Enclosed Front Controls

Cylindrical Stainless Steel Burner

Appliance Grade Finish

Raypak XPak Residential

Hydronic Heating Boilers	Model

Note:

1.	    DHW capability provided via following options:  three way valve or pump and indirect tank

Raypak, Inc. 2151 Eastman Avenue, Oxnard, CA  93030 (805) 278-5300 Fax (800) 872-9725   www.raypak.com

# Text boxes

# Condensing 90+

# XPak™ Residential

## Hydronic Heating Boilers

## Models 85 &120

AFUE Ratings

| Model | AFUE |
| --- | --- |
| 85 | 90.3 |
| 120 | 90.5 |

Models 85 &120